## Slide 1: A Method to Implement Low Energy Read Operations, and Single Cycle Write after Read in Subthreshold SRAMs
The Subthreshold Group
Arijit Banerjee
Dated: 12/10/2012
VLSI
6332 Project

## Slide 2: Why Operate SRAMs in Subthreshold Supply Voltages?
Reducing is costly in terms of design effort
For low frequency (in kHz) medical circuits, Vdd scaling to subthreshold voltages is very effective

## Slide 3: Known Problems in 6T based Subthreshold Bitcells
For 6T based 8T, 9T 10T…
  Read stress SNM in half selected cells while writing
  No column muxing is a must
  Writeback (two cycle write after read ) is a must in writing

## Slide 4: How to Lower Energy Further in 6T Based Subthreshold SRAMs?
Possibly voltage scaling?
  Voltage scaling further? Not a good idea!
  Vmin is limited by worst case HSNM, VDRV, and so on

## Slide 5: Vmin Dependency
Worst case μ - 3σ hold SNM for 6T based 10T
Worst Case
MIT 180xlp data provided by James Boley BSN Chip Group @ UVa

## Slide 6: Vmin Dependency
Worst case μ + 3σ data retention voltage (VDRV)
Worst Case
IBM 130nm data provided by James Boley BSN Chip Group @ UVa

## Slide 7: Possible Solutions to “How to Lower Energy in 6T Based Subthreshold SRAMs”
New type of bitcells
Novel read/write methods
New SRAM architectures

## Slide 8: Earlier Works in SRAM Dynamic Energy/Power Mitigation

## Slide 9: Can We do Better?
Using RAS-CAS DRAM timing concept in SRAM
Low Energy Read (LER)?
  Do not operate decoders, word line drivers
“N-1” distinct LER operations per one read in N word row
Auto detection of LER

## Slide 10: Single Cycle Write after Read(WAR)?
Earlier approach was two cycle write after read
Our approach is single cycle write after read
  Using intermediate latch to latch the read row before write
  Pulsed read and write word line generation in WAR
  Controllable WAR margins through external pins

## Slide 11: Block Diagram of the 4KB Subthreshold Data Memory
128 to 16-bit Bus Interface Logic
Global Bitline Mux/Demux
Memory Array 4 Banks X 1 KB
Precharge and column Circuitry
128-bit Intermediate Latch
Row and Bank Decoders
Column Decoders
Address Input Flops
Write after Read Control, Timing Control, LER Support Logic, and Power Control Logic
11-bit Address Bus
Control Signals
16-bit Input Bus
16-bit Output Bus

## Slide 12: Energy Comparison: Read vs. LER in IBM 130nm Technology
Chart: Comparison of Read Energy @ 0.3V 27C with LER Energy @ 0. 5V 27C in 4KB Subthreshold Memory
LER Energy @ 0.5V 27C TT | 2.4727e-13
Read Energy @ 0.3V 27C TT | 7.3921e-13
LER Enrgy @ 0.5 27C FF | 2.8649e-13
Read Energy @ 0.3v 27C FF | 7.3133e-13
3X
Savings
2.5X Savings
LER Energy @ 0.5V 27C FF

## Slide 13: Subthreshold LER Energy Savings Trend in IBM 130nm Technology
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 4KB Subthreshold SRAM
| 0.3 | 0.35 | 0.4 | 0.45 | 0.5
TT | 9.5949 | 6.4126 | 4.5935 | 7.4935 | 7.0085
FF | 2.2929 | 5.5362 | 3.5572 | 5.3138 | 6.4597
SS | 2.8151 | 5.117 | 6.0926
FS | 1.6743 | 6.8129 | 7.3541
SF | 4.8797 | 4.5251 | 5.9856 | 5.7227
Chart: LER Energy Savings vs. Supply Voltage @ 27C in 4KB Subthreshold SRAM
| 0.4 | 0.45 | 0.5
TT | 4.5935 | 7.4935 | 7.0085
FF | 3.5572 | 5.3138 | 6.4597
SS | 2.8151 | 5.117 | 6.0926
FS | 1.6743 | 6.8129 | 7.3541
SF | 4.5251 | 5.9856 | 5.7227

## Slide 14: Penalty in Our Method
7% area
3% worst case standby leakage
25% worst case WAR energy
45% worst case read energy
Enough room in cycle time with worst case of 1.03 MHz for kHz domain operation

## Slide 15: Comparison With Prior Works

## Slide 16: Status of the VLSI 6332 Project

## Slide 17: Conclusions
No need to operate SRAMs in deep subthreshold voltages
Worst case 5.7X LER energy savings in KHz frequencies @ 0.5V 27C
Seven distinct LER operations per one read in eight word row
WAR margins are externally controllable
Penalty of 7% area, 3% worst case standby leakage, 25% worst case WAR energy, and 45% worst case read energy in design change

## Slide 18: References
[1] J. P. Kulkarni, K. Kim, and K. Roy, “A 160 mV Robust Schmitt Trigger Based Subthreshold SRAM,” IEEE Journal of Solid-State Circuits, vol. 42, no. 10, pp. 2303–2313, Oct. 2007.
[2] I. J. Chang, J.-J. Kim, S. P. Park, and K. Roy, “A 32 kb 10T Sub-Threshold SRAM Array With Bit-Interleaving and Differential Read Scheme in 90 nm CMOS,” IEEE Journal of Solid-State Circuits, vol. 44, no. 2, pp. 650–658, Feb. 2009.
[3] T. H. Kim, J. Liu, J. Keane, and C. H. Kim, “A high-density subthreshold SRAM with data-independent bitline leakage and virtual ground replica scheme,” in Solid-State Circuits Conference, 2007. ISSCC 2007. Digest of Technical Papers. IEEE International, 2007, pp. 330–606.
[4] B. H. Calhoun and A. Chandrakasan, “A 256kb sub-threshold SRAM in 65nm CMOS,” in Solid-State Circuits Conference, 2006. ISSCC 2006. Digest of Technical Papers. IEEE International, 2006, pp. 2592–2601.
[5] G. K. Reddy, K. Jainwal, J. Singh, and S. P. Mohanty, “Process variation tolerant 9T SRAM bitcell design,” in Quality Electronic Design (ISQED), 2012 13th International Symposium on, 2012, pp. 493–497.
[6] Ali Valaee, Asim J. Al-Khalili, “SRAM Read-Assist Scheme for High Performance Low Power Applications” in International SoC Design Conference (ISOCC ) on , 2011, pp. 179-182.
[7] S. Yoshimoto, M. Terada, S. Okumura, T. Suzuki, S. Miyano, H. Kqwaguchi and M. Yoshimoto, “A 40-nm 0.5-V 20.1-µW/MHz 8T SRAM with Low-Energy Disturb Mitigation Scheme,” in IEEE Symposium on VLSI Circuits Digest of Technical Papers on, 2011, pp. 72-73.
[8] Atsushi Kawasumi, Toshikazu Suzuki, Shinich Moriwaki and Shinji Miyano, “ Energy Efficiency Degradation Caused by Random Variation in Low-Voltage SRAM and 26% Energy Reduction by Bitline Amplitude Limiting (BAL) Scheme,” in IEEE Asian Solid-State Circuits Conference on, 2011, pp. 165-168.
[9] Mohammad Sharifkhani, Manoj Sachdev, “A Low Power SRAM Architecture Based on Segmented Virtual Grounding,” in International symposium on Low Power Electronics and Design (ISLPED) on, 2006, pp. 256-261.
[10] A. Kawasumi, Y. Takeyama, O. Hirabayashi, K. Kushida, F. Tachibana. Y. Niki, S. Sasaki and T. Yabe, “Energy Efficiency Deterioration by Variability in SRAM and Circuit Techniques for Energy Saving without Voltage Reduction,” in IC Design & Technology (ICICDT), 2012 IEEE International Conference on, 2012.
[11] Mohammed Shareef I, Pradeep Nair, Bharadwaj Amrutur, “Energy Reduction in SRAM using Dynamic Voltage and Frequency Management,” in 2008 21st International Conference on VLSI Design on, 2008, pp. 503-508.
[12] http://download.micron.com/pdf/datasheets/psram/8mb_asyncpage_p23z.pdf
[13] http://www.issi.com/pdf/41C-LV16256C.pdf
[14] http://www.chiplus.com/Uploads/DataSheet/Pseudo%20SRAM/Pseudo_CS26LV32163%20(2.7).pdf

## Slide 19: Acknowledgments
Grad students @ BSN chip team: James Boley , Yousef Shakhsheer, Alicia Klinefelter, Yanqing Zhang, Kyle Craig, Peter Beshay
Mateja Putic, grad student, UVa
Gary Lee, SEAS IT administrator
Professor Mircea Stan, ECE, UVa
Professor Ben Calhoun, ECE, UVa

## Slide 20: Thank You! Questions?